## Slide 1: EECS 388: Embedded Systems Lecture 8
Instructor: Tamzidul Hoque, Assistant Professor, Dept. of EECS, University of Kansas (hoque@ku.edu), office: Eaton 2038
Credits: Some slides are adopted from Henk Corporaal’s Computer Architecture and Organization course
and also from CS232: Computer Architecture II. University of Illinois at Urbana-Champaign.

## Slide 2: Context
Chapter 4:Introduction to Computing Systems: From Bits & Gates to C & Beyond, Yale Patt
Machine Language (ISA)
Digital Logic
Electronic Circuits
Transistors
Compiler
Application Program
Operating
System

## Slide 3: Illustration of CPU Datapath for MIPS
How this architecture operates for:
Fetch
Decode
Execute
Memory
Write Back

## Slide 4: Initial State
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address

## Slide 5: Fetch
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 6: Fetch:
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
Program counter starts from 0
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 7: Fetch
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
Inst mem gets 0 as input, outputs the content at address 0
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 8: Fetch
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
Content at address 0 is the first instruction
add $t0, $t1, $t2
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 9: Decode for Add
add $t0, $t1, $t2
9
Inst 25-21, rs
Inst 20-16, rt
Inst 15-11, rd
Inst 15-0, imm

## Slide 10: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
Instruction gets broken down into segments and goes to register and control units
add
$t2
$t0
$t1
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 11: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
Control signals are asserted
add
$t2
$t0
$t1
Select Rt
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 12: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
Register data Rs and Rt comes out
add
$t2
$t0
$t1
40
60
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 13: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
ALU Performs Add
add
$t2
$t0
$t1
40
60
Do Add
60
100
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 14: Mem
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 0
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
Mem stage only needed for Load Store
add
$t2
$t0
$t1
40
60
60
100
No read/Write
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 15: Write Back
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
0
add $t0,
$t1, $t2
Write Back the result to $t0
add
$t0
100
Select ALU out
100

## Slide 16: Anytime
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
4
Update PC to PC+4 before next fetch
add
Not a branch
PC+4

## Slide 17: Fetch Next Inst
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
4

## Slide 18: Fetch:
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
Register
Inst. Memory
Data
Address
F
D
EXE
Mem
WB
4
Program counter starts from 0
40 | 0
44 | 0
48 | 0
Data Memory
Data
Address

## Slide 19: Execution process of Second Instruction

## Slide 20: Fetch
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
4
sw $s0, 4($t1)
Inst mem gets 4 as input, outputs the content at address 4

## Slide 21: Fetch
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
4
sw $s0, 4($t1)
Content at address 4 is the first instruction
sw $s0, 4($t1)

## Slide 22: Decode for SW/LW
sw $s0, 4($t1)
Inst 25-21, rs
Inst 20-16, rt
Inst 15-11, rd
Inst 15-0, imm
Base
Offset

## Slide 23: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
4
sw $s0, 4($t1)
Instruction gets broken down into segments and goes to register and control units
sw
$t1
$s0
4

## Slide 24: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
Control signals are asserted
Select Imm
4
sw $s0, 4($t1)
sw
$t1
$s0
4

## Slide 25: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
Register data comes out
40
4
4
sw $s0, 4($t1)
sw
$t1
$s0
4
200

## Slide 26: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
ALU Performs Add
add
Do Add
40
4
4
sw $s0, 4($t1)
sw
$t1
$s0
4
200
44

## Slide 27: Decode
0 | 
4 | 
8 | 
add $t0, $t1, $t2
sw $s0, 4($t1)
beq $s1, $s2, 24
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Inst. Memory
Data Memory
Data
Address
Data
Address
F
D
EXE
Mem
WB
Store data to address 44
add
Do Add
40
4
4
sw $s0, 4($t1)
sw
$t1
$s0
4
200
44
200

## Slide 28: Example Question
$t0 | 100
$t1 | 40
$t2 | 60
$s0 | 200
$s1 | 
$s2 | 
40 | 0
44 | 0
48 | 0
Register
Data Memory
Data
Address
Calculate the values in the box after all stages of instruction sw $s0, 4($t1) are done?
?
?
?

## Slide 29: Case Study: Atmel ATmega168
Atmel ATmega168 datasheet
8 bit data bus

## Slide 30: Case Study: Atmel ATmega168
Atmel ATmega168 datasheet
8 bit data bus
PC
Register File
ALU
IR
Control Unit
Instruction Memory
Data Memory
IO

## Slide 31: Recap
Von Neumann computer model